## Slide 1: Vehicle Adaptations
Road to Independence
April 8, 2024
Stephen Kinstler
United Access

## Slide 2: What do Automotive Mobility Equipment Dealers do?
  Provide solutions to achieve independence through mobility.
    Accessible Vehicles (Vans, Trucks, Cars, etc)
      Transport drivers or passengers that remain seated in a wheelchair or scooter
    Scooter and Wheelchair Lifts
      Transport unoccupied wheelchairs and scooters
    Driving Controls and Aids
      Hand controls, high tech driving controls, transfer seats, left foot accelerators, etc.
    Mobility Seats
      Help ease entry and egress from vehicle
Notes: We provide solutions that help people achieve freedom and independence.
  Accessible Transportation, Vans, etc.
    Transports drivers or passengers that are seated in mobility devices
  Lifts for scooters and power chairs
  Mobility Devices
    Hand controls, high tech driving controls, transfer seats, left foot gas pedals, etc.
    Here at United Access – we go beyond that – we also help provide our customers with a community – work with accessible sports programs, etc to help our customers achieve not only transportation but the ability to do the things they love!
Here at United Access – we go beyond that – we also help provide our customers with a community – work with accessible sports programs, etc to help our customers achieve not only transportation but the ability to do the things they love!
Here at United Access – we go beyond that – we also help provide our customers with a community – work with accessible sports programs, etc to help our customers achieve not only transportation but the ability to do the things they love!

## Slide 3: Who Do Mobility Dealers Work with?
Who Do Mobility Dealers work with?
Disabling Diseases and Conditions
Amyotrophic Lateral Sclerosis – ALS – Lou Gehrig’s Disease
Cerebral Palsy - CP
Muscular Dystrophy - MD
Multiple Sclerosis - MS
Post-Polio
Spina Bifida
Stroke
Amputation
Mobility issues related to aging process
Injury-related Disabilities:
Brain Injury
Spinal Cord Injury – SCI
Traumatic Amputation

## Slide 4: The Mobility Process… a Road Map for Independence
The Mobility Process
Diagnosis – Long Term Needs/Short Term Needs
Assessment with your Mobility Dealer/Funding
Entry/Egress Needs, Durable Medical Equipment Used
Driver Evaluation
Equipment

## Slide 5: Mobility Dealer Assessment
Needs Analysis
  Nature of the disability
  Walking aids or Mobility equipment used
  Current vs. Long-term diagnosis
  Abilities/Stature:
    Driver/Non-driver
    Abilities and/or Physical Limitations
    Seated Height (Top of head to floor while seated in a wheelchair)
  Lifestyle
    Daily ease
    Traveler
    Family size or number of passengers
  Funding

## Slide 6: Equipment Options
Scooter & Wheelchair Lifts
Mobility Seating
Lowered-floor minivans
Full-size vans
Truck Conversions
Driving controls
Lock down devices

## Slide 7: Scooter and Wheelchair Lifts Stow an unoccupied wheelchair or scooter
Benefits
  Applicable to many vehicle types
  Can be switched from one vehicle to another, with some limitations
  Low cost option
Compromises
  Will not accommodate all scooters, power wheelchairs or vehicles.
  Patient needs to be ambulatory or have a care-taker
  May lose vehicle seating
  Less flexible as condition changes
  Not a large resale market

## Slide 8: Vehicle Lifts
Basic Lift Types:
External Lift (platform and wheeled)
Boom/Interior Lift
Interior Platform Lift
Boom/Interior Lift
External Lift
Interior Platform Lift

## Slide 9: Mobility Seating Providing Ease of Entry into the Vehicle
Benefits
Applicable to many vans, minivans and SUV’S
  Eases entry into a taller vehicle
  No drill installation to increase re-sale value
  Removable, can be transferred to other vehicles with some limitations
Compromises
  370 lb weight capacity
  Still need to stow wheelchair, if applicable
  Not able to work in many driver’s areas
  Speed of entry and egress is limited

## Slide 10: Options for seat transfer
Link by Adapt Solutions
Turny EVO by BraunAbility

## Slide 11: How does a wheelchair accessible minivan differ from a standard minivan?
A lowered-floor (10 to 14 inches) increases door opening height, creating ease of entry for wheelchair users and greater interior height inside the vehicle.
Removable Driver and Front Passenger seats.
Multiple positioning options for comfort (Driver, Passenger, middle area position).
Middle row seats are removed for interior maneuverability.
A power kneeling system decreases ramp angle to allow a smooth transition upon entry and exit of vehicle.
One-touch entry system.

## Slide 12: Lowered-Floor Minivan Side-entry
Foldout Ramp
Infloor Ramp

## Slide 13: Wheelchair Accessible Minivan Advantages & Disadvantages
Benefits
  Can ride or drive from your wheelchair
  Flexible seating arrangements
  Long-term Solution
  Resale opportunity
Compromises
  Vehicle Selection Limitations
  Limited Passenger Capacity
  Limited towing options
  No all-wheel drive options*
  Expense

## Slide 14: Full-Size Van Adaptations Available
A lowered-floor to increase door opening height and interior height for wheelchair users.
Raised Roof to increase interior height.
Raised Door to increase door opening height.
Door operators and Lift to accommodate an
occupied wheelchair.
Transfer seats available.

## Slide 15: Full Size Van Advantages & Disadvantages
Benefits
  Many customizations possible
  Additional storage areas
  Initial costs
  Towing Capabilities
  Weight Capacity
Compromises
  Gas mileage
  Maneuverability & Parking
  Speed of entry/egress
  Customizations can be expensive
  Less of a re-sale market

## Slide 16: Options
Side Entry
Rear Entry
Chassis:
Ford Transit
Ram Promaster
Mercedes Sprinter
Options:
Standard Top
High Top
Standard Wheelbase
Extended Wheelbase
Conversion Vans

## Slide 17: Additional Vehicle Modifications (Truck Conversions)
ATC Conversions
Access a Top Pickup Conversion

## Slide 18: Additional Vehicle Modifications

## Slide 19: Steering Devices

## Slide 20: High Tech Driving Controls

## Slide 21: The Future of Mobility
Hybrid Vehicles – Currently available on the 2021 Toyota Sienna and Up. Other manufacturers to follow.
Electric Vehicles – In development at this time. As States legislate a move towards electric vehicles, the mobility industry is facing significant challenges in developing this technology for accessibility.
Autonomous Vehicles – Offers tremendous promise but will not be available until there is a suitable chassis with enough room for a wheelchair seated passenger.

## Slide 22: FAQ
How much do vehicle adaptations cost?
Are there used equipment or vehicles available?
Can you rent a wheelchair accessible van?
How long does the process take?
Does insurance cover vehicle modifications?

## Slide 23: For questions or further information, we are available at your convenience.
United Access
888.939.1010
Stephen Kinstler
816-471-0305
Steve.Kinstler@unitedaccess.com